## Slide 1
B1 RESIDUAL REINFORCEMENT LEARNING - Introduction
PI
(Baseline)
+
Plant
(Motor+Rod)
RL Policy
Clip to
Residual Reinforcement Learning for Speed Control
A pure PI controller compensates the speed error but ignores gravity and the nonlinear dynamics of the system. Adding a feedforward term requires an accurate physical model. The residual approach lets us learn that correction directly from interaction with the system, with no knowledge of the motor parameters.
Fig. 1 - The policy does not replace the PI; it adds a bounded correction on top. Safety is guaranteed by design: |ΔV|≤3.6V and the total voltage never exceeds ±12V.
Agent | Neural Network (SAC) learning
Environment | BDC Motor + rod simulated at 1 kHz
State s | Speed error, velocity,
Action a | (bounded)
Reward r | − − effort penalty − rate penalty
Objective | Accurate tracking, smooth control
Agent | 
Environment | BDC Motor + rod simulated at 1 kHz
State s | 
Action a | 
Reward r | 
Objective | 
Main advantage. The policy learns what the PI cannot model (feedforward and gravity compensation) without ever seeing the motor equations.

## Slide 2
B2 RESIDUAL REINFORCEMENT LEARNING - Framework
State Observer
 | Speed error, normalised | Primary tracking signal, tells the policy how far off we are
 | Current speed, normalised | Captures the current operating point and back-EMF regime
 | Rod angles (2 variables) | Encodes the gravity load
 | Reference speed, normalised | Lets the policy distinguish a ramp from a step, anticipate the next operating point
 | PI output, normalised | Tells the policy what the baseline already commands, this is what makes the control residual
 | Speed error, normalised | Primary tracking signal, tells the policy how far off we are
 | Current speed, normalised | Captures the current operating point and back-EMF regime
 | Rod angles (2 variables) | Encodes the gravity load
 | Reference speed, normalised | Lets the policy distinguish a ramp from a step, anticipate the next operating point
 | PI output, normalised | Tells the policy what the baseline already commands, this is what makes the control residual
, a moderately large tracking error; maps typical errors to , saturation errors to
, just above the maximum reference (); keeps all speed features in [-1, 1]
All six features are clipped to [-10, 10] before entering the network, no unbounded inputs
It is the interface between the system and the neural network.
At every step it collects raw measurements and converts them into the input vector. It does three things:
— selects only the variables needed to compute ΔV, discarding everything else;
— normalises each quantity so that training is numerically stable;
— re-encodes the rod angle as (sin θ, cos θ) to avoid the discontinuity at ±π.
The observer is minimal by design: 6 scalars, no history, no raw sensor data. The policy has exactly what it needs to compute the missing feedforward and nothing more.

## Slide 3
B3 RESIDUAL REINFORCEMENT LEARNING - Framework
Reward Function
The reward function is the only channel through which the policy learns what "good control" means:
It is computed at every policy step (every 10 ms) and has three terms:
First
Tracking Term
It penalises the mean absolute speed error averaged over the ten sub-steps between policy updates.
Second
Effort term
It penalises large residuals, keeping the PI in charge and preventing the policy from issuing unnecessary corrections.
Third
Rate Term
It penalises how much the correction changes between consecutive updates, suppressing chattering and producing a smoother voltage profile.
We use the absolute value (L1) rather than the squared error (L2) because L1 weights small persistent errors more uniformly and is less sensitive to large transient spikes, on this problem it reduced the trajectory RMSE from 0.172 to 0.081 rad/s compared to L2.
The weights and are roughly 100 times smaller than the tracking term (), they shape the action without ever competing with the primary objective.

## Slide 4
B4 RESIDUAL REINFORCEMENT LEARNING - Training
Training & Test set
Unlike supervised learning, there is no fixed dataset collected in advance. The policy trains online: at every step it interacts with the simulated motor, receives a reward, and updates its weights. The "dataset" is the distribution of speed references the environment samples during training.
Training set (12 references, fixed seed)
To evaluate the trained policy on in-distribution references we freeze a set of 12 profiles sampled from the same distribution used during training. Each profile is one of three types drawn at random:
— Constant, a fixed target speed held for the full 5 s episode;
— Quintic ramp, a smooth minimum-jerk transition from one speed to another, with random start time and duration;
— Multi-step, 2 to 4 piecewise-constant levels with random edges and amplitudes.
All references are drawn from , matching the training range.
Test set (7 held-out references, never seen during training)
The test set is designed to probe three failure modes: constant references at 6, −5 and 12 cover different operating points including negative speeds; two quintic ramps (2→9 and 0→ -8 ) and one step drop (8→3 rad/s) verify that generalisation holds across profile shapes and directions. The hardest probe is a constant at 14 , beyond the training range, where any performance is pure extrapolation and the strongest evidence against overfitting.

## Slide 5
B5 RESIDUAL REINFORCEMENT LEARNING - Training
Neural Network Architecture
The correction the PI is missing depends on rod angle, operating speed, and reference profile in a nonlinear way and the input is a vector of six physical scalars with no spatial structure and no temporal ordering. An MLP is the natural choice: it learns an arbitrary smooth mapping from to with no inductive bias that would conflict with the problem structure.
MLP Policy Network — π_θ : ℝ⁶ → [−1, 1]
INPUT LAYER
6 features
HIDDEN LAYER
64 units · ReLU
OUTPUT LAYER
1 unit · tanh
e / e_s
ω / ω_s
sin θ
cos θ
ω* / ω_s
V_base / V_max
x₁
x₂
x₃
x₄
x₅
x₆
·
·
·
× 64 units total
tanh
ΔV
∈[−1,1]
ReLU
tanh → [−1, 1]
W₁ ∈ ℝ⁶⁴ˣ⁶
W₂ ∈ ℝ¹ˣ⁶⁴
Total trainable parameters: 6×64 + 64 + 64×1 + 1 = 513
One hidden layer and 64 units residual is a smooth, low-dimensional correction, this is sufficient to approximate it.
ReLU activation, piecewise-linear, no vanishing gradient, standard for continuous-action SAC policies.
tanh output, squashes the network output to (-1, +1) regardless of weight magnitude, the residual limit is enforced by the architecture, not by clipping after the fact.

## Slide 6
B6 RESIDUAL REINFORCEMENT LEARNING - Validation
Saturation and Residual Authority: Design Choice
The residual authority is a deliberate design choice, not an optimised hyperparameter. The reasoning is physical: the two corrections the PI is missing are the gravity compensation and the steady-state feedforward. Together they sum to at most comfortably within the window. Setting δ too small would prevent the policy from correcting what the PI misses; setting it too large would let the policy override the baseline and risk destabilising the loop. 30% is the conservative choice that covers the physically meaningful corrections while keeping the PI in charge.
The saturation is managed at three levels:
Architecture
tanh bounds ΔV The output neuron passes through tanh, so always and regardless of weight values. The policy cannot saturate the residual channel even if it tries.
Control Law
Hard clip before the motor , PI and policy are summed first, then clipped. Neither component alone can push the motor beyond the hardware rail.
PI anti-windup
Prevents integrator blow-up The integrator is clamped so . Without this, a sustained error during a transient would wind the integrator to an arbitrarily large value, causing a slow oscillatory recovery once the error clears.
In our operating regime (references up to 12 rad/s), the total voltage touches the rail for only 0.1–0.4 % of the time, brief spikes at step changes. Saturation is not a limiting factor here. For higher speeds where rail contact becomes frequent, a saturation-aware observation mode is available: the state gains a seventh feature , the policy can sense the rail and avoid wasting effort against it

## Slide 7
B7 RESIDUAL REINFORCEMENT LEARNING - Validation
Machine Learning Validation: Train Vs Test set
This is a regression problem, the network outputs a continuous voltage correction, not a class label. We report four metrics on the tracking error :
— MAE, mean absolute error: average magnitude of the tracking error
— RMSE, root mean squared error: primary control metric, penalises large deviations more
— R², fraction of the reference variance explained by the achieved speed; defined only for time-varying references
— in-band %, fraction of time with ; the honest analogue of "accuracy" for a continuous tracking task
Set | MAE | RMSE | R2 | In-band %
Train (12 references) | 0.069 | 0.292 | 0.955 | 99.7%
Test (7 held-out) | 0.080 | 0.240 | 0.996 | 99.8%
Result. Test error is no worse than train on every metric, the policy has not memorised the training references, it has learned a general control strategy. R2 improves on the test set because held-out references are smoother and easier to track than the random multi-step profiles used during training. The gap between train and test RMSE goes in the safe direction: no overfitting.

## Slide 8
B8 RESIDUAL REINFORCEMENT LEARNING - Validation
Ablation Study: Network Depth and Seed Robustness
To verify that the architecture choice is not arbitrary and the results are not seed-dependent, we trained 3 architectures × 3 random seeds = 9 independent models and evaluated each on the held-out test set. All models use the same reward, hyperparameters and training budget (300k steps).
Architecture | RMSE | R2 | In-band %
MLP [64] |  | 0.996 | 99.8%
MLP [256,256] |  | 0.995 | 99.8%
MLP [256,256, 256] |  | 0.996 | 99.8%
Architecture | RMSE | R2 | In-band %
MLP [64] |  | 0.996 | 99.8%
MLP [256,256] |  | 0.995 | 99.8%
MLP [256,256, 256] |  | 0.996 | 99.8%
Depth does not help. The smallest network achieves the lowest RMSE. Adding layers and parameters makes performance slightly worse, the residual is a smooth, low-dimensional function that a shallow network approximates just as well, with less risk of overfitting the training distribution.
The result is robust, not lucky. The per-seed standard deviation for [64] is ±0.001, negligible. The [256,256] network shows higher variance (±0.004), meaning deeper models are more sensitive to initialisation. The multi-seed experiment confirms that the improvement over pure PI is a structural property of the residual architecture, not an artefact of a fortunate random seed.

## Slide 9
B9 RESIDUAL REINFORCEMENT LEARNING - Validation
Closed-Loop Performance: Benchmark
All three controllers run on the same simulated plant, same references, same noise model. Performance is measured on the held-out test set, 7 references never seen during training, to avoid any information leak between the RL training and the evaluation.
Controller | MAE | RMSE | R2 | In-band %
PI (Baseline) | 0.281 | 0.411 | 0.988 | 85.2%
PI + poly + grav | 0.046 | 0.222 | 0.997 | 99.8%
RL residual | 0.078 | 0.240 | 0.997 | 99.8%
RL residual reduces the pure PI tracking error by 75% (RMSE 0.411 → 0.240) and closes most of the gap to the strong classical baseline (0.240 vs 0.222), without any knowledge of the motor parameters or the gravity model. The in-band percentage jumps from 85% to 99.8%, matching the feedforward controller exactly on that metric.
The residual does not fully match PI + poly + grav on RMSE. This is expected: the classical controller uses the exact physical model; the policy approximates it from data alone. The remaining gap (0.018 rad/s) is the cost of being model-free.

## Slide 10
B10 RESIDUAL REINFORCEMENT LEARNING - Validation
Closed-Loop Performance: Controller Comparison
Each panel shows the achieved speed (blue) against the reference (dashed red) for one controller and one reference profile. RL Residual follows the reference closely on the quintic trajectory, where the PI alone shows a persistent steady-state offset, the learned ΔV compensates what the integrator cannot correct fast enough.

## Slide 11
B11 RESIDUAL REINFORCEMENT LEARNING - Validation
Closed-Loop Performance: Voltage Decomposition
Total motor voltage for each controller. Bottom: the RL residual split into (PI baseline, blue) and (learned correction, orange). During transients ΔV is the dominant term, so the policy has implicitly learned the feedforward and gravity compensation that the PI baseline cannot provide.